LEDTask™ Super High Output LTR1200-24-HO  24VDC  Linear Ribbon Installation Instructions using DTC and DTW-series connectors

*MAKE SURE LEDTask AMPERAGE DOESN’T EXCEED POWER SUPPLY*

****ONLY USE 24 VOLT POWER SUPPLIES****

Make all connections and test system before installing

MAX RUN  ON A SINGLE POWER LEAD FOR =  16.4 feet.

- Cutting the LED ribbon to desired length: Using scissors the LED ribbon can be cut on the clearly marked cutting line which is located every 6 LEDS, except where the solder drops are located on the ribbon. The solder is located every 19-1/2 inches on the ribbon. Making a cut anywhere else on the ribbon except on the cutting line will cause damage to the circuit and the ribbon will not operate properly.

- Connecting ribbon to power supply. Using the DTW- connector, peel back the paper on the ribbon leaving the double stick tape in place, pull the wedge out, slide the ribbon into the crimp connector, making sure to fully insert the ribbon into the connector and close the connector tightly until it seats. Verify the polarity is correct.   Test connection for continuity.

- Connecting cut ribbon sections together.   Using the DTC- at end of the first reel, pull the wedge out, peel back the paper on the ribbon leaving the double stick tape in place, slide the ribbon into the crimp connector, making sure to fully insert the ribbon into the connector; repeat the process for the ribbon that is being connected to the first ribbon. Push the wedge in squarely and tightly on both ends. Verify polarity is correct. Test connection for continuity.

- Make sure to verify polarity and continuity before installing the ribbon. The DTC connector and ribbon have a proper electrical orientation and cannot be “flipped” or put on upside down.

Cut on designated cut marks only	             Peel backing from ribbon	                        Pull wedge out

Align polarities, slide ribbon into connector, seat ribbon in fully and push the wedge in fully