LEDTask™ LTR300, 300-100, LTR60 -,   Reel Linear Ribbon Installation Instructions using LTC-EZ and LTW-EZ connectors

**MAKE SURE LEDTask AMPERAGE DOESN’T EXCEED POWER SUPPLY**

****ONLY USE Proper VOLT DC POWER SUPPLIES****

Make all connections and test system before installing

MAX RUN  ON A SINGLE POWER LEAD FOR  std output =  32.8FT.  ltr300- =  16.4 FT

- Cutting the LED ribbon to desired length: Using scissors the LED ribbon can be cut on the clearly marked cutting line which is located every 6 LEDS except where the solder drops are located on the ribbon. The solder is located every 19-1/2 inches on the ribbon. Making a cut  anywhere else on the ribbon except on the cutting line will damage the circuit and the ribbon will not operate properly.

- Connecting ribbon to power supply. Using the LTW-EZ- connector, open the snap cover, slide the ribbon into the snap connector, making sure to fully insert the ribbon under the side tabs and under the metal contacts.  Verify the polarity is correct.   Test connection for continuity, close the EZ Snap connector tightly until it seats.

- Connecting  cut ribbon sections together.   Using the LTC-EZ snap connector at end of the first reel, open the snap cover and slide the second ribbon under the side tabs, under the metal contacts.  Test connection for continuity, Close the snap cover tightly.

- Make sure to verify polarity, and continuity, The EZ connector and ribbon have a proper electrical orientation and cannot be “flipped” or put on upside down.

Cut on designated cut marks only.	Peel backing from ribbon.	     Align polarities and slide ribbon into connector.

(LTW-EZ-24”) ribbon to power.

Seat ribbon in fully and snap cover closed.  	      Slide ribbon fully under the contacts,   (LTC-EZ-1”)